## Slide 1
Utilisation of waste gas from BF stove

## Slide 2
Mentor- Dr. Prakash Bansi Abhale(Iron making)
Waste for plant
Poison for environment.
Category- Utilisation of waste gas (CO2+N2) from
blast furnace stoves
Proposal- Reaction of CO2 in waste gas with low
grade aluminium dross to convert into
useful CO and alumina.
Team- Adarsh Raj, Onkar Pushp( BIT Sindri)

## Slide 3
In Ironmaking, BF top gas is burnt in stoves to heat the incoming cold blast and the flue gas containing CO2 and N2 are released to atmosphere through chimney after removal of all the possible heat and dust.
This is leads to production of tons of CO2 daily.
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 57 | 42.2 | 0 | 0
N2
52.7%
47.3%
Dry Stove Gas
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 50 | 24 | 22 | 4
N2
H2
About 50%
About 24%
About 22%
(4%)
Blast furnace gas
After burning in O2
Schematic Greenhouse Effect
For TATA STEEL
243 million ton CO2 daily
303 million ton N2 daily

## Slide 4
Aim-
Our aim is to utilise this waste gas(CO2+N2).
All together nature has provided
118 elements.
But utilisation will be easy if the elements
could be oxidised in CO2 environment.
For utilisation we have to convert them into
usable form using various chemical reactions.
And metals are the best reducing agents.
But metals with heavy nucleus cannot be used because of low specific energy.
Moreover, the metal used should be cheap and in abundant amount.
This narrows our search to only two metals- Aluminium and Zinc.

## Slide 5
Why aluminium?
Since aluminium is the most abundant metal found on earth’s crust.
Moreover it is a better reducing agent than zinc.
500⁰ C
900⁰ C
700⁰ C
1000⁰ C
Reaction rate(1/s)
Environment | Substance | Size(micron) | Time (ms) | %Exp error
Air | Aluminium | 165 | 75 | 9.3
CO2 | Aluminium | 165 | 45 | 11.2
Combustion Time( ref: Rossi, Dreizin & law2001)
Moreover, its has very high conversion of CO2 into useful CO.

## Slide 6
Idea
Aim :
The aim is to use waste CO2 from blast furnace stoves for the production
of Alumina and Carbon Monoxide using cheap aluminium dross.
Comparison with Hall Heroult process:
Al2O3 + 1.5 C → 2 Al + 1.5 CO2
Hall heroult-
Proposed reaction:
Al + 1.5 CO2 → 0.5 Al2O3 + 1.5 C (500C)
Heating above 900C:
Al + 1.5 CO2
→
0.5 Al2O3 + 1.42 CO+ traces of carbon
Our idea is exactly reverse of Hall Heroult Process
Hall Heroult extracts Al from Alumina(found in bauxite)
Our idea converts Al of Aluminium dross into alumina
using waste CO2 gas and gives CO as a byproduct which
is useful for steel industry.

## Slide 7
Introduction
1
2
3
Current Situation
1. Charge ( Sinter + Coke ) is
fed at the top of the Blast
Furnace
2. Exhaust gas from the top is
cleaned using a system of
Scrubbers, Cyclone
Separators etc.
Then the exhaust gas is burnt
in Regenerative Stoves to
preheat the incoming blast

## Slide 11
Literature Review
D. S. Sundarama, V. Yanga and V. E. Zarkob,
Y Liu, H Ren, Q J Jiao
Experiment
Oxidation mechanism of micron-sized aluminum particles in Al-CO2 gradually heating system in a DSC
Ref: IOP Conf. Series: Materials Science and Engineering 248 (2017) 012002
Experiment
Experimental data from several sources were gathered to elucidate the effect of the particle size on the flame temperature of nano-sized aluminum particles.
Ref: Translated from Fizika Goreniya i Vzryva, Vol. 51, No. 2, pp. 37–64
Rossi, Dreizin & Law
Experiment
A micro-arc GEnerator of Monodispersed Metal Droplets (GEMMED) was used to generate uniform droplets of Al metal which is then oxidized to Al2O3
Ref: Combust. Sci. and Tech., 2001. Vol. 164. pp. 209-237
Xiaoying Zhu, Mirko Schoenitz, and Edward L. Dreizin (NJIT, 2009)
Experiment
Micron-sized Al particles were subjected to varied heating rates and XRD was used for analysis of the sample.
Ref: J. Phys. Chem. C 2009, 113, 6768–6773
Environment | Substance | Size(micron) | Time (ms) | %Exp error
Air | Aluminium | 165 | 75 | 9.3
CO2 | Aluminium | 165 | 45 | 11.2
Combustion Time( ref: Rossi, Dreizin & law2001)
Experiment
A 20-L apparatus was used to determine 3 dust explosion characteristics: Pmax, (dp/dt)max and MEC .
International Journal of Chemical Engineering
Volume 2010, Article ID 941349, 6 pages
doi:10.1155/2010/941349
Hong Chun Wu

## Slide 12
Proposed Process Flow Diagram
1
2
3
4
Current Situation
1. Charge ( Sinter + Coke ) is
fed at the top of the Blast
Furnace
2. Exhaust gas from the top is
cleaned using a system of
Scrubbers, Cyclone
Separators etc.
Then the exhaust gas is burnt
in Regenerative Stoves to
preheat the incoming blast
The exhaust gas from the stoves
is fed to a Reactor

## Slide 17
Use FactSage™ to establish Thermodynamics of the process
Conduction of a Crude experiment in Dry Ice
Conducting TGA of samples of Aluminium and it’s dross
SEM of the TGA sample
Flue gas analysis using Blast Furnace Simulator
Reactor Design
Work Plan

## Slide 18: Thermodynamic Results
REACTION TEMP( ⁰C) | PRODUCTS ( in moles ) |  |  |  |  |  | ∆H | ∆G | ∆S
 | N2(gas) | CO2(gas) | CO(gas) | GRAPHITE(s) | Al2O3(s) |  |  |  | 
500 | 0.78918 | 0.18377 | 2.71 × 10-2 | 0.73286 | 0.5 |  | -4.89 × 105 | -6.521 × 105 | -6.33 × 101
550 | 0.77683 | 0.16525 | 5.79 × 10-2 | 0.71272 | 0.5 |  | -4.83 × 105 | -6.71 × 105 | -5.15 × 101
600 | 0.75693 | 0.1354 | 0.10767 | 0.6788 | 0.5 |  | -4.68 × 105 | -6.91 × 105 | -3.76 × 101
650 | 0.73103 | 9.65 ×10-2 | 0.17243 | 0.63206 | 0.5 |  | -5.54 × 105 | -7.12 × 105 | -2.19 × 101
700 | 0.70527 | 5.79 ×10-2 | 0.23681 | 0.58211 | 0.5 |  | -4.39 × 105 | -7.33 × 105 | -6.41
750 | 0.68645 | 2.96 × 10-2 | 0.28386 | 0.54324 | 0.5 |  | -4.26 × 105 | -7.56 × 105 | +6.41
800 | 0.67596 | 1.39 × 10-2 | 0.31 | 0.52063 | 0.5 |  | -4.17 × 105 | -7.78 × 105 | 1.601
850 | 0.67098 | 6.47 × 10-3 | 0.32255 | 0.50964 | 0.5 |  | -4.08 × 105 | -8.022 × 105 | 2.34 × 101
900 | 0.66873 | 3.09 × 10-3 | 0.32817 | 0.50463 | 0.5 |  | -4.01 × 105 | -8.25 × 105 | 2.96 × 101
950 | 0.6677 | 1.55 × 10-3 | 0.33075 | 0.50232 | 0.5 |  | -3.94 × 105 | -8.49 × 105 | 3.52 × 101
1000 | 0.66721 | 8.16 × 10-4 | 0.33197 | 0.50122 | 0.5 |  | -3.88 × 105 | -8.73 × 105 | 4.04 × 101

## Slide 19: Kinetic Results
The results obtained from TGA are strictly in accordance with theoretical results
The graph rises exponentially from 650 degrees upto 1200 degrees

## Slide 23
Vision and Benefits of our Idea
The cost of fossil fuels will exponentially rise in future
and thus the iron making process.
The exponential rise in the rate of CO2 is really a threat
In long term. Moreover, due to its high density CO2 will
definitely reside where humanity exists.
Our idea of conversion of CO2 into CO will definitely help in lowering global warming rate because it is not
just limited to steel industries but can be used in any CO2 emitting industry.
The CO produced during this process will help in reducing the amount of coke consumption and thus
it might be helpful in decreasing the cost expenses in long run.